| Section 1: General |
| --- |
| Company Name: | Requestor’s Name: Cell Phone: |
| Task Location: | Task Description: |
| Expected Start Date: | Expected Completion Date: (Not to exceed 7 days) |
| If you answer “YES” to any of questions 1-4 below STOP - contact your supervisor and your company EHS/ Competent Person to evaluate the space, the entry, and the work. The space MAY be considered a Permit Required Confined Space by your company, and your company may require a Confined Space Entry Permit before entry and any work begins. |
| Are you planning to remove a floor tile, enter, and work under the raised floor with no open floor tile(s) directly above the individual(s) and/or work area(s)? No or Yes |
| Will the raised floor entry and/or work being performed under the floor contain and/or create a potential safety or health hazard(s) (e.g., hazardous atmosphere, using inert gas and/or chemicals, HPM line breaking, HPM liquid or residue in the work area under the raised floor, demolition, engulfing an entrant, welding, energized electrical work, other recognized serious safety or health hazard)? No or Yes |
| Is there anything that will restrict egress or trap the entrant from under the raised floor (e.g., screwed down tiles, exhaust lines, piping)? No or Yes |
| Are you planning to go under equipment that may create a potential safety or health hazard (e.g., hazardous atmosphere, energized robotics, process equipment, noise that hinders communications)? No or Yes |
| Ensure a buddy/spotter is present at all times during entry. No working alone. |
| Ensure a guardrail system (e.g., a top-rail at least 39 inches in height above the walking-working surface, capable of supporting a force of 200 pounds, a mid-rail set halfway between the top-rail and the walking-working surface capable of withstanding a force of 150 pounds, a gate at the entranceway, and a toe-board that is 3.5 inches vertical height) is secured and signage is present and set-up around the floor opening(s). Exception: If one (1) floor tile is removed for work lasting fifteen (15) minutes or less, a spotter individual must constantly guard the floor opening to alert others to the open floor. A soft barrier consisting of danger tape and signs must also be installed around the floor opening area. |
| Ensure the appropriate PPE and equipment is present before doing any work under the raised floor (e.g., tile puller, personal fall protection system, hard hat/bump cap, flashlight, gloves, eye protection, knee pads). |
| Always try to remove/open floor tiles that are directly above the individual(s) and/or work area(s). |
| Stay within the site-required twelve (12) foot distance (6 tiles) of the raised-floor tile opening(s) while working under the raised floor. |
| Obtain approval signatures from the persons specified below… |
| Complete Section 2 below. |
| Give notification to affected individuals in the work area. |
| Post this Floor Tile Removal Form at the entry point(s) to the raised floor opening(s). |

| Position | Name (Print) | Signature | Date |
| --- | --- | --- | --- |
| Contractor EHS Representative or Competent Person N/A |  |  |  |
| Tenant EHS Representative or Competent Person N/A |  |  |  |
| Entrant / Floor Tile Remover |  |  |  |
| Entrant / Floor Tile Remover |  |  |  |
| Spotter / Buddy (If Entry is Required) |  |  |  |
| Supervisor or Designated Representative |  |  |  |
| NY CREATES / SUNY Poly EHS N/A (When NY CREATES staff remove floor tiles and/or are entrants) |  |  |  |
| Other N/A |  |  |  |

| Section 2: Click the Check Box for Setup Details |
| --- |
| Fab Level or Data Center: | Click Check Box as Planned |
| Guardrail system used with danger warning signs: | Yes |
| One (1) spotter individual to guard the one (1) removed floor tile, with danger warning signs and tape, for work lasting fifteen (15) minutes or less: N/A | Yes |
| Notification(s) given to affected individuals in the work area: | Yes |
| Tethers used and in place for parts/tools: N/A | Yes |
| Objects positioned away from opening(s): N/A | Yes |
| Mandatory supervision required: | Yes |
| Personal fall protection system required: N/A | Yes | No |
| Sub Fab Level: N/A | Click Check Box as Planned |
| Soft barrier used with danger warning signs and danger tape: | Yes |
| Notification(s) given to affected individuals in the work area: | Yes |
| Additional requirements and/or comments: |