| Monitoring Completed By: | Monitoring Date & Time: |
| --- | --- |
| Title: | Department: |
| Employee Supervisor/Title: | Monitoring Equipment Used: MiniRAE 3000 (P/N: 059-4020-000) |
| Description Work Area: Solvent waste storage system (NFN WWT1 / WWT2) | Equipment Calibration: Isobutylene - 100 PPM |
|  | Calibration Date: |
| Calibration Information: |
| In accordance with Reference Method 21, the two NIST gas cylinder mixtures that are used for instrument calibration are: (1) Grade Zero Air calibration gas - Scott Calibration Gas. P/N: 077-0091. (2) Calibration Gas - isobutylene 100 ppm. Certificate of calibration: Instrument serial # 592-901840. Model # PGM-7320. Cylinder calibration expiration date: 4/2012. |
| Calibration Precision Test Completed: Test Results: Zero Air calibration precision = %. Isobutylene Calibration Gas calibration precision = %. Response Time Test Completed: Test Results: Average response time = seconds. ( % final stable reading) |
| Monitoring Information: |
| Air sampling was conducted to monitor potential solvent waste leaks in and around the solvent waste storage system located in NFN Waste Water Treatment Level 1 (WWT1) and Waste Water Treatment Level 2 (WWT2). Air sampling was conducted during normal operation. Air sampling was collected according to Reference Method 21 - Determination of Volatile Organic Compound Leaks (EPA Federal Regulation). The air sampling measurements were taken using a RAE MiniRAE 3000 portable monitor. Unit set to monitor IPA. |
| Sampling: |
| The instrument probe shall be traversed around all potential leak interfaces as close to the interface as possible as described in Reference Method 21. Sampling was completed around all: Flanges, Discharge Lines, Solvent Tank Inlets, Tank Flanges, Sump Pump Lines, Sump Pump Flanges, Tank Drains, Solvent Unload Lines, Discharge Flanges, Solvent Exhaust lines, Pressure Vents, and Flame Arrestors. |

| Date Inspected | VOC Reading | Location of Equipment (WWT1 N2-SW-T-01) | Equipment ID # | Type of Equipment | Leak Detected (>500 PPM)? (Y/N) | Expected Date of Repair (if leak detected) | Corrective Action (if necessary) | Inspector | Initials |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Solvent Waste Line inlet | F-1 | Flange |  |  |  |  |  |
|  |  | Solvent Waste Line inlet | F-2 | Flange |  |  |  |  |  |
|  |  | Solvent Waste Line inlet | F-3 | Flange |  |  |  |  |  |
|  |  | Solvent Waste Line inlet | F-4 | Flange |  |  |  |  |  |
|  |  | Steel Waste Line inlet | F-5 | Flange |  |  |  |  |  |
|  |  | Steel Waste Line inlet | F-6 | Flange |  |  |  |  |  |
|  |  | Flame Arrestor | FA-1 | Flame Arrestor |  |  |  |  |  |
|  |  | Tank Flange (level transmitter) | TF-1 | Flange |  |  |  |  |  |
|  |  | Tank Flange (level transmitter) | TF-2 | Flange |  |  |  |  |  |
|  |  | Steel Line Discharge | DL-1 | Steel Fitting |  |  |  |  |  |
|  |  | Steel Line Discharge | DL-2 | Steel Fitting |  |  |  |  |  |
|  |  | Sump Pump | N2-SW-P01 | Sump Pump |  |  |  |  |  |
|  |  | Steel Line Discharge | DL-3 | Steel Fitting |  |  |  |  |  |
|  |  | Steel Line Discharge | DL-4 | Steel Fitting |  |  |  |  |  |
|  |  | Pulsation Dampner | PD-01 | Steel Enclosure |  |  |  |  |  |
|  |  | Steel Line Discharge | DL-5 | Steel Fitting |  |  |  |  |  |
|  |  | Steel Line Discharge | DL-6 | Steel Fitting |  |  |  |  |  |
|  |  | Steel Line Discharge | DL-7 | Steel Fitting |  |  |  |  |  |
|  |  | Steel Line Discharge | DL-8 | Steel Fitting |  |  |  |  |  |
|  |  | Steel Line Sump | SL-1 | Steel Fitting |  |  |  |  |  |
|  |  | Steel Line Sump | SL-2 | Steel Fitting |  |  |  |  |  |
|  |  | Steel Line Sump | SL-3 | Steel Fitting |  |  |  |  |  |
|  |  | Pulsation Dampner | PD-02 | Steel Enclosure |  |  |  |  |  |
|  |  | Steel Line Sump | SL-4 | Steel Fitting |  |  |  |  |  |
|  |  | Steel Line Sump | SL-5 | Steel Fitting |  |  |  |  |  |
|  |  | Sump Pump | N2-SW-P02 | Sump Pump |  |  |  |  |  |
|  |  | Sump Flange Discharge | SF-1 | Steel Fitting |  |  |  |  |  |
|  |  | Flange Discharge | DF-1 | Flange |  |  |  |  |  |
|  |  | Flange Discharge | DF-2 | Flange |  |  |  |  |  |
|  |  | Flange Discharge | DF-3 | Flange |  |  |  |  |  |
|  |  | Flange Discharge | DF-4 | Flange |  |  |  |  |  |
|  |  | Flange Discharge | DF-5 | Flange |  |  |  |  |  |
|  |  | Flange Discharge | DF-6 | Flange |  |  |  |  |  |
|  |  | Solvent Exhaust | SE-1 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Exhaust | SE-2 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Exhaust | SE-3 | Steel Fitting |  |  |  |  |  |
|  |  | Pressure Relief Vent Flange | SE-4 | Steel Fitting/Enclosure |  |  |  |  |  |
|  |  | Pressure Relief Valve/Conservation Vent | PVR-01 | Steel Enclosure |  |  |  |  |  |
|  |  | Pressure Relief Vent Flange | SE-5 | Steel Fitting/Enclosure |  |  |  |  |  |
|  |  | Solvent Exhaust | SE-6 | Stainless/Steel Fitting |  |  |  |  |  |
|  |  | Solvent tank inlet | SI-1 | Flange |  |  |  |  |  |
|  |  | Solvent tank inlet (solvent inlet) | SI-2 | Flange |  |  |  |  |  |
|  |  | Tank Flange | TF-1 | Flange |  |  |  |  |  |
|  |  | Tank Flange (level transmitter) | TF-2 | Flange |  |  |  |  |  |
|  |  | Tank Flange (level transmitter) | TF-3 | Flange |  |  |  |  |  |
|  |  | Tank Flange (spare) | TF-4 | Flange |  |  |  |  |  |
|  |  | Tank Overflow Drain | TF-5 | Flange |  |  |  |  |  |
|  |  | Rupture Disk Flange | TF-6 | Flange |  |  |  |  |  |
|  |  | Waste SUMP (P-04 Discharge) | TD-1 | Steel Fitting |  |  |  |  |  |
|  |  | Waste SUMP (Discharge) | TD-2 | Steel Fitting |  |  |  |  |  |
|  |  | Waste SUMP (Discharge) | TD-3 | Steel Fitting |  |  |  |  |  |

| Date Inspected | VOC Reading | Location of Equipment (WWT2 N2-SW-T-02) | Equipment ID # | Type of Equipment | Leak Detected (>500 PPM)? (Y/N) | Expected Date of Repair (if leak detected) | Corrective Action (if necessary) | Inspector | Initials |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  | Waste SUMP (Discharge) | TD-4 | Steel Fitting |  |  |  |  |  |
|  |  | Pulsation Dampner | PD-03 | Steel Enclosure |  |  |  |  |  |
|  |  | Tank Drain (Discharge) | TD-5 | Steel Fitting |  |  |  |  |  |
|  |  | Waste SUMP (Discharge) | TD-6 | Steel Fitting |  |  |  |  |  |
|  |  | Waste SUMP (Discharge) | TD-7 | Steel Fitting |  |  |  |  |  |
|  |  | Sump Pump | N2-SW-P04 | Sump Pump |  |  |  |  |  |
|  |  | Waste SUMP (Discharge) | TD-8 | Steel Fitting |  |  |  |  |  |
|  |  | Waste SUMP (Discharge) | TD-9 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Line (P-03/intake) | SUL-1 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Unload Line (storage) | SUL-2 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Unload Line (storage) | SUL-3 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Unload Line (storage) | SUL-4 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Unload Line (storage) | SUL-5 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Unload Line (storage) | SUL-6 | Steel Fitting |  |  |  |  |  |
|  |  | Sump Pump | N2-SW-P03 | Sump Pump |  |  |  |  |  |
|  |  | Solvent Unload Line (storage) | SUL-7 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Unload Line (storage) | SUL-8 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Unload Line (storage) | SUL-9 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Unload Line (storage) | SUL-10 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Unload Line (storage) | SUL-11 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Pressure Relief Valve | SUL-12 | Steel Fitting |  |  |  |  |  |
|  |  | Pulsation Dampner | PD-04 | Steel Enclosure |  |  |  |  |  |
|  |  | Solvent Unload Line (storage) | SUL-13 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Unload Line (storage) | SUL-14 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Vent/Flame Arrestor | STE-1 | Steel Fitting |  |  |  |  |  |
|  |  | Detonation Flame Arrestor | DFA-1 | Steel Enclosure |  |  |  |  |  |
|  |  | Solvent Vent/Flame Arrestor | STE-2 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Vent/Flame Arrestor | STE-3 | Steel Fitting |  |  |  |  |  |
|  |  | Pressure Relief Valve/Conservation Vent | PVR-02 | Steel Enclosure |  |  |  |  |  |
|  |  | Solvent Vent/Flame Arrestor | STE-4 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Tank Exhaust (storage) | STE-5 | Steel Fitting |  |  |  |  |  |
|  |  | Solvent Tank Exhaust (storage) | STE-6 | Steel Fitting |  |  |  |  |  |
| NOTES: |  |  |  |  |  |  |  |  |  |  |
| F: Flange |  | SE: Solvent Exhaust |  | SL: Sump Line | STE: Solvent Tank Exhaust |
| DF: Discharge Flange | SF: Sump Flange |  | TF: Tank Flange |  | SUL: Solvent Unload Line |
| DL: Discharge Line | SI: Solvent Tank Inlet |  | TD: Tank Drain |  | Not Detected - <500 PPM |
| Comments: |
| Corrective Action Taken: (Must be within 5 days of finding a leak): (i.e., tightened bolts/flange/fitting, reseating of gaskets, fitting, etc.) |