ERT Contact: Day 1 (518-956-1287 / 518-729-8504) or Day 2 (518-410-8685 / 518-410-1559)

| Start Date: | End Date: |
| --- | --- |
| Location of Work: |
| Type of Work: |
| NY CREATES Work Sponsor & Phone Number: |
| Permit Requestor Name, Phone Number & Company: |
| Qualified Tool Operator’s Name & Phone Number: |
| Operator’s Certification/License Number: |
| Type of Power-Actuated Equipment: |
| Size of Charge (for powder type) and Fastener Type: |
| Make, Model, and Serial Number of Tool: |
| Required PPE: |

SUBMIT 2 COPIES OF THE WORK PERMIT, POWER-ACTUATED PERMIT, AND 2 COPIES OF THE 
OPERATOR’S CERTIFICATION AT THE WORK AUTHORIZATION PERMIT MEETING.

Do Not Write Below This Line – FOR NY CREATES ERT/EHS USE ONLY – Do Not Write Below This Line

Safety Requirements for Power-Actuated Tools - Mark each box for compliance.

BEFORE THE WORK - All of the following precautions must be taken:

Ensure area is cordoned off to prevent unauthorized access during power-actuated fastener activities. This includes ensuring no one is behind the area of work before using the tool.

Power-actuated tools must be inspected, handled and used in compliance with OSHA 29 CFR, 1926.302, and 1910.243.

Any proposed use of power-actuated tools must be approved by and coordinated with the NY CREATES Work Sponsor. Prior to the use of said tool the employee or contractor must obtain all applicable permits.

Power-actuated tools must be operated only by those who are certified or licensed for, and trained in the operation of the particular tool being used.

The type and size of fastener to be used must only be those specifically manufactured for use in such tools and compatible with the type and size of material which the fasteners are to be driven into.

Power-actuated tools must not be used in explosive or flammable atmospheres.

Power-actuated tools must not be loaded until just prior to the intended use time.

DURING THE WORK – The operator agrees that All of the following precautions will be taken:

Loaded power-actuated tools must never be left unattended.

Power-actuated tools must never be pointed at anyone.

Spent and misfired cartridges must be disposed of in accordance with manufacturer instructions.

Appropriate Personal Protective Equipment must be used.

If applicable: Protective shields, guards, jigs, or fixtures must be designed and built by the tool manufacturer.

Tools may only be operated on the approved date(s), area(s) specified, and person(s) named on the permit.

This permit has been reviewed with and understood by the power-actuated tool operator before the 
commencement of work activities.

| Power-Actuated Tool Operator Signature | Date |
| --- | --- |

| ERT/EHS Signature |  | Date |
| --- | --- | --- |