SECURITY DISPATCH:  518-437-8600

| Inspection Date Requested: | Duration of Work: |
| --- | --- |
| Location of Scaffold: |
| Purpose of Scaffold: |
| Permit Requestor & Phone #: |
| NY CREATES Work Sponsor & Phone #: |
| Designated Competent Person Name & Phone #: |
| Type of Scaffold: |
| Max. Material Weight on Scaffold: | Max # of Workers on Scaffold: |

TO BE FILLED OUT BY DESIGNATED COMPETENT PERSON PRIOR TO ERT/EHS INSPECTION:

I have sufficient experience and knowledge to recognize scaffold hazards, correct unsafe conditions, and shut down the worksite until any hazards are corrected.

A Personal Fall Arrest System (PFAS) and/or an approved guardrail system is in place 
(both may be used if working from different work surfaces).

Sign off is required each day of use by the company’s designated Competent Person(s).

All employees are properly trained.

I have examined the work location, scaffold, and components and declare it safe and ready for use.

Competent Person: _______________________  _____________________ Date:_____________

(Print)				    (Signature)

TO BE FILLED OUT BY ERT/EHS PRIOR TO SCAFFOLD USE (Call Security Dispatch and request ERT.)

| ERT/EHS Name: | Date of Inspection: |
| --- | --- |
| General Rules for Scaffolds | YES | NO | Comments |
| Is the scaffold tagged and indicates maximum intended load and signed off? Green Yellow Red |  |  |  |
| If the scaffold is defective, has it been removed from service and RED tagged out? |  |  |  |
| Are there any restrictions on the tag? Please list: |
| Scaffold is fully planked - No more than 1” gap between planks. |  |  |  |
| Planking is overlapped at least 12” or secured from movement. |  |  |  |
| Planking must extend at least 6” and no more than 12” past the support end (no more than 18” on planks longer than 10’). If not, planking must be secured (cleated or restrained) to prevent sliding. |  |  |  |
| Guardrail System: Top Rail (38” inch to 45” inch) Mid Rail Toe board (min of 4”) |  |  |  |
| Scaffold is 14” or less from face of work, if workers remove front guardrails (18” for plasterers). |  |  |  |
| If no mesh present between toe board and planking, is barrier in place to prevent people from working / walking under scaffold? |  |  |  |
| Work platform free of clutter, mud, snow, oil or any trip hazards? |  |  |  |
| Tools and material being lifted with the use of a bucket or tag line? |  |  |  |
| Minimum power line clearance (10 feet) - If NO, is the power off? |  |  |  |
| Work area clear of mechanical (crush) hazards? |  |  |  |
| Are riggers secured and installed correctly? |  |  |  |
| General Rules for Supported Scaffolds |  |  |  |
| Height-to-base width ratio: Less than 4:1 (no guying, ties, or braces required) |  |  |  |
| Over 4:1 (scaffolds are restrained from tipping by guying, tying, or bracing) |  |  |  |
| All scaffold frames and uprights use base plates (mud sills required if on dirt). |  |  |  |
| Footings are level, sound, and rigid. No settling may occur. |  |  |  |
| Unstable objects such as blocks, bricks, buckets, etc., are not used as work platforms or to support scaffolds. |  |  |  |
| Platform is at least 18” wide (12” on pump jacks). |  |  |  |
| Additional Rules for Mobile Scaffolds |  |  |  |
| Platform is at least 20” wide. |  |  |  |
| Casters are locked before work begins. |  |  |  |
| Pathways to work locations are on even ground, clear of obstructions, away from doors and other hazards. |  |  |  |
| General Rules for Access |  |  |  |
| No more than 2’ step up or down or a 14” step across to get on or off a platform. |  |  |  |
| Ladder first rung is not more than 24” above the ground (hook on and Attachable Ladders). |  |  |  |
| Hook-on and attachable ladders are designed for the scaffold. |  |  |  |
| Rungs line-up vertically for the entire height of the scaffold. |  |  |  |
| Is access provided by an attached ladder to a point of access that is guarded by gates, removable rails, or chains? |  |  |  |
| Cross braces are not used for fall protection or access/egress. |  |  |  |
| ERT/EHS Requirements |  |  |  |
| ERT/EHS has issued Permit Identification Sign. |  |  |  |

Designated Competent Person: 	______________________  _______________________

(Print) 					(Signature)

Company Name: 	__________________________

ERT / EHS: _____________________________________                 		Date: _____________
(Signature)