The following form shall be completed and reviewed prior to proceeding with any maintenance or cleaning activities in the cleanroom on tools that contain hazardous production materials (HPMs) or contain materials that, if emitted, have a high degree of risk associated with them, such as foreline cleanings. HPMs are materials that have a degree-of-hazard rating in health, flammability, or reactivity of Class 3 or 4 as ranked by the National Fire Protection Agency.

| Maintenance approval Form |
| --- |
| Requested By: | Date of Request: |
| Tool Owner and Contact Info: | Contact Info for person responsible for maintenance activity: |
| Name of Organization: | Date and Time of Activity: |
| Tool Identification | Work Description Details |
| Tool Name, Hex #, and Chamber ID: |  |
| Why is maintenance requested: |  |
| Description of proposed maintenance: |  |
| Number of Pump and Purge cycles to be completed: |  |
| List all materials which have been processed in the tool/chamber as they appear on the Approved Chemical List: |  |
| Expected task duration: |  |
| What companies are completing the work: |  |
| What specific parts will be inspected, removed, replaced, or cleaned: |  |
| Additional Scope of Work details: |  |
| Chamber Opening Guide |
| TOOL MUST REMAIN IN MAINTENANCE MODE WHEN FORELINE IS CLEANED IN PLACE |
| ANY MODIFICATION OR TEMPORARY BYPASS OF THE SCRUBBER REQUIRES EHS PRE-APPROVAL |
| Set up caution tape barrier and post signage at a minimum of ten feet (10’) from the maintenance area. Snorkel Exhaust: If applicable, install adequate local exhaust ventilation. Wear appropriate PPE, including respiratory protection. Place tool in maintenance mode and notify Security. Follow established procedures. Verify all cycle purges are performed prior to opening. Collect samples at each location and document: At OPERATOR’S breathing zone for 1 minute; (NOTE: paper tape detectors need longer detection time) At SNORKEL EXHAUST after 5 minutes; In AMBIENT AIR after chamber has been fully opened. Label hazardous waste and dispose properly. |